www.DanaherMotion.com

CD20 Technical Information

The CD20 is built from two electronic boards:

Digital board is either the digital board used in all CD series 5 drives or the digital board used in the synqnet drive. This document does not cover the digital board.

Power board is designed for 20 ARMS and 40 ARMS for two seconds. This document covers the technical information for the ordering part number and power board information.

## Ordering Information

Possible part numbers are:

CE20561 – CD series 5, 20 ARMS continuous, Incremental encoder feedback, SERCOS interface

CR20560 – CD series 5, 20 ARMS continuous, Resolver feedback, Analog Interface

LB20565 – Synqnet Drive, 20 ARMS continuous, sine encoder feedback, Synqnet Interface

## Input Power Filtering

The SERVOSTAR CD electronic system components require EMI filtering in the input power leads to meet the conducted emission requirements for the industrial environment. This filtering blocks conducted-type emissions from exiting onto the power lines and provides a barrier for EMI on the power lines.

Be sure to adequately size the system. The type of filter is based on the voltage and current rating of the system the incoming line is three-phase. These filters are mounted as close to the incoming power as possible so noise is not capacitively coupled into other signal leads and cables. These lines may be noisy, so separate them from other sensitive cabling to avoid unwanted coupling of noise. Several manufacturers of these filters are listed below. They should be able to recommend the best filter design for most typical motor control applications. Danaher Motion also provides specific filter recommendations that adequately attenuate the conducted noise to levels well below the CE limits. Implement the EMI filter according to the following guidelines:

— Mount the filter on the same panel as the drive.

— Mount the filter as close as possible to the incoming cabinet power.

— When mounting the filter to the panel, remove any paint or material covering. Use an unpainted metallic back panel, if possible.

— Filters are provided with an earth connection. Tie all ground connections to ground.

— Filters can produce high leakage currents. Earth filters before connecting the supply!

— Do NOT touch filters for 10 seconds after removing the supply.

Recommended EMI Line Filter for CD20

Schaffner FN3258-30-47 http://www.schaffner.com Schaffner Holding AG Nordstrasse 11 CH-4542 Luterbach Switzerland T +41 32 6816 626 F +41 32 6816 641

CORCOM http://www.corcom.com Telephone 847-680-7400 For Customer Service please call 1-800-468-2023 FAX 847-680-8169 Postal address 844 E. Rockland Road Libertyville, Illinois 60048

Fair-Rite http://www.fair-rite.com Telephone (888) FAIRRITE (324-7748) or (845)895-2055 FAX (888) FERRITE (337-7483) or (845) 895-2629 Postal address PO Box J, 1 Commercial Row Wallkill, NY 12589

## Outline Dimensions

## Cx20 System Wiring

### (CD Series 5)

### Cx20 (Cx2056y)

### Lx20 (Synqnet)

## Hardware Specifications

| Amplifier Model | Cx20 |
| --- | --- |
| Unit Weight | Lbs./Kgs. | 8.8 / 4 |
| Mounting Hardware | English (Metric) | 10-32 (M4) |
|  | Applied Torque | 20 lb-in. (2.26 N-m.) |
| Connection Hardware | Line Screw Size/Torque | M3.5/12 lb-in. (1.35 N-m) |
|  | BUS Screw Size/Torque |  |
|  | Motor Screw Size/Torque |  |
|  | Ground Screw Size/Torque |  |
| Wire Size (AWG#) | Control Logic (AWG/ mm2) | 16 / 1.31 |
|  | Configurable I/O wire gauge | 22-18 AWG (0.3-0.75 mm2) Ferrules recommended: 18 AWG Type H0 - 75/14 Weidmuller 4629.0 or equivalent 20 AWG Type H0 - 5/14 Weidmuller 6907.0 or equivalent 22 AWG Type H0 – 34/12 Weidmuller 90257.7 or equivalent |
|  | Regen (AWG/ mm2) C B+ | 10 / 5.26 |
|  | Motor Line (AWG/ mm2) Main Input Ma Mb Mc L1 L2 L3 | 10 / 5.26 |
| Clearance Distance | Side-to-Side | 0.5 in (12.7 mm) |
|  | Top/Bottom | 2.5 in (63.5 mm) |
| Mating Connector Hardware | CK100 Kit | Includes: C1, C2, C4, C7 (plus 2 ft./0.69 m. of stranded bus ribbon), C8 |
|  | C1 | D9 Female EDA 8S0009SS402S25 Connector 9 pins D type for Cable solder |
|  | C2 | D25 Male EDA 8S0025SS402525 Connector 25 pins D Type For Cable solder |
|  | C3 | Danaher Motion #: A-93899-013 Vendor Info: Weidmuller BL3.5/13 Cat.No. 161574 |
|  | Connector Screw Torque | 2.25 lb-in. (0.25 N-m) |
|  | C4 | D9 male or Sercos or RJ45 for synqnet EDA 8S0009SS402S25 Connector 9 pins D type for Cable solder Sercos matting connector come w/ the sercos cable RJ45 shielded Ethernet cable |
|  | C7 | 10 Pin (0.1”x0.1”) Female ribbon |
|  | C8 | D9 male EDA 8S0009SS402S25 Connector 9 pins D type for Cable solder |
|  | C9 | 20 PIN connector HIROSE FX2BA-20SA-1.27R |
|  | Regen (AWG/ mm2) C B+ | Connector: 2 x PIN Molex MiniFit Molex P/N 42816-0212 *Terminal (Pins): Molex P/N 42815-0031 |
|  | Motor Line (AWG/ mm2) Main Input Ma Mb Mc L1 L2 L3 | Connector: 6 x PIN Molex MiniFit Molex P/N 42816-0612 *Terminal (Pins): Molex P/N 42815-0031 |
|  | 24 V Logic (optional) | Danaher Motion #:A-81014-002 Vendor Info: PCD ELFP02210 |

* Molex Crimp tooling P/N 63811-1500 for terminal pins

## Electrical Specifications

| Product Model | Cx20 |
| --- | --- |
| Main Input Power | Voltage (VACL-L) Nominal (10% | 180 to 230 3( only |
|  | Line Frequency Hz | 47-63 |
|  | Input power at 180 VAC L-L | 5.3 kW |
|  | Input power at 208 VAC L-L | 6.2 kW |
|  | Input power at 230 VAC L-L | 6.8 kW |
|  | Continuous Current (A) | 20 A/phase |
|  | Peak Current (A) for 2s | 40 A/phase |
|  | Line Fuses (FRN-R, LPN, or equiv.) | 25 |
| Logic Input Power | +24 VDC Ext. Logic Voltage (V) | 22 to 27 |
|  | +24 VDC Ext. Logic Current (amps sink) | 1.5 |
|  | +24 VCD Ext. Logic Current (amps max surge) | 2.6 |
| SoftStart | Max. Surge Current (A) | 200 |
|  | Max. Charge Time (msec) | 50 |
| Protection Functions | Fault Contact Rating (A) | 1 |
|  | Fault Contact Closing Period (ms) | Close = 3 ms, Open = 2 ms |
|  | Over-Temperature Trip ((C/(F) | 80/176 |
| Rated Main Output (Ma, Mb, Mc) | Continuous Power at 180 VAC L-L Line Input (45(C (113(F) Ambient) | 4 kW |
|  | Continuous Power at 230 VAC L-L Line Input (45(C (113(F) Ambient) | 5.2 kW |
|  | Continuous Current (ARMS) | 20 |
|  | Peak Current (Arms) for 2 sec | 40 |
|  | PWM Frequency (kHz) | 8 |
|  | PWM Motor Current Ripple (kHz) | 16 |
|  | Form Factor (rms/avg) | (1.01 |
| Protective Functions | Under-Voltage Trip (nominal) (VDC) | 100 |
|  | Over-Voltage Trip (VDC) | 400 |
|  | Over-Temperature Trip ((C/(F) | 80/176 |
|  | Internal heat dissipation (watts) | 330 |
| Environment | Operation temperature ((C/(F) | 5/41 to 45/113 |
|  | Storage temperature ((C/(F) | 0/32 to 70/158 |
|  | Ambient humidity (%) | 10 to 90 |
|  | Atmosphere | without corrosive gasses or dust |
|  | Altitude | Derate 5% per 1000 ft.(300 m) above 3300 ft. (1000 m) |
|  | Vibration (g) | 0.5 |

## Regen Information

| Product Model | Cx20 |  |  |
| --- | --- | --- | --- |
| External Shunt Regulator | Peak current (amps) | 45 |
|  | Minimum resistance (ohms) | 4 at 190VBUS / 8 at 320VBUS |
|  | watts | 1 kW |
|  | BUS Voltage (nominal) (VDC) | 325 |
|  | VHYS (Regen circuit turn-off) (VDC) | 375 |
|  | VMAX (Regen circuit turn-on) (VDC) | 385 |
| External Regen Kits | TBD | ( | ( | ( |

## CD20 Series 5 TOP View

## CD20 Series 5 Mating Connectors

## Customer Support

Danaher Motion products are available world-wide through an extensive authorized distributor network. These distributors offer literature, technical assistance, and a wide range of models off the shelf for the fastest possible delivery.

Danaher Motion sales engineers are conveniently located to provide prompt attention to customer needs. Call the nearest office for ordering and application information and assistance or for the address of the closest authorized distributor. If you do not know who your sales representative is, contact us at:

Danaher Motion

203A West Rock Road

Radford, VA 24141 USA

Phone: 1-540-633-3400

Fax: 1-540-639-4162

Email: customer.support@danahermotion.com

Website: www.DanaherMotion.com